## Slide 1
MARITIME CYBER RANGE
01 / 05
Unmanned Ships Can Be Hacked
Maritime Cyber Range -- a testbed for attacking and defending autonomous vessels
Unmanned surface and underwater vehicles are the future of naval ops.
Fewer crews, longer missions, lower cost -- navies worldwide are adopting them.
They run on GPS, AIS, and radio commands -- all of it is forgeable.
None of these signals were designed with an attacker in mind.
A spoofed GPS fix or a replayed command can silently steer a real vessel.
No alarms, no warning -- the vehicle just believes the lie.
There was no easy way to test, end-to-end, whether a given vessel would resist this.
This project builds a tool that answers that question, with evidence.

## Slide 2
MARITIME CYBER RANGE
02 / 05
We Built a Cyber Range to Find Out
Real autopilot software, real physics, four digital-twin vehicles
Real ArduPilot + Gazebo physics.
The same flight-control software used on real hardware.
Two real Navy vehicle designs, twinned.
A mine-hunting surface boat and an underwater mine-hunting AUV.
Each vehicle: vulnerable + hardened.
Same hardware, one has basic security hygiene switched on.
The hardened twin proves defenses work.
A side-by-side, apples-to-apples security comparison.
THE FOUR TWINS
Fleet-class USV (surface) + REMUS-100 AUV (underwater) -- each as a vulnerable / hardened pair

## Slide 3
MARITIME CYBER RANGE
03 / 05
Attack, Then Watch What Happens
Three real attacks, launched from the dashboard, scored by a blind detector
GPS / acoustic-position spoofing -- feed the vehicle a false location.
Surface vehicles get forged GPS; the AUV gets a forged acoustic position fix.
AIS spoofing -- impersonate or ghost another vessel on the radio.
Tests whether nearby traffic reporting can be faked convincingly.
Command replay / injection -- resend or forge autopilot commands.
Can an attacker seize control by replaying or injecting MAVLink commands?
A rule-based detector watches every attack blind -- it never sees attack ground truth.
Answers two separate questions: did it work, and would anyone notice?

## Slide 4
MARITIME CYBER RANGE
04 / 05
The Results, Proven Live
Every result below came from a real, live run -- not assumed
VULNERABLE
on every tested attack
mode-change, RC-override, GPS spoof (where physically possible)
RESILIENT
attacker couldn't succeed
mode-change blocked outright; RC-override never got far enough to arm
0s -- 11s
detection latency
instant for GPS/AIS; ~10s for C2 (a measurement-window design choice, not a gap)
Every attack was blocked or stopped before it could start.
Same physical vehicle, same mission -- security hygiene alone made the difference.
The whole pipeline works on any ArduPilot-based vehicle, not just ours.
Point the tool at someone else's autopilot and get the same verdict + report.

## Slide 5
MARITIME CYBER RANGE
05 / 05
Why It Matters
A reusable answer to a question every autonomous fleet will be asked
A reusable testing tool, not a one-off demo.
Point it at any ArduPilot vehicle and get a real vulnerability report.
A clear, defensible verdict every time -- never a guess.
Four possible outcomes: vulnerable, resilient, inconclusive, or not applicable.
Cheap, safe, and fast to run before a vehicle ever touches water.
Simulation-first testing catches problems before they're expensive to fix.
Next up: finish the AUV fix, then test two new attacks.
Navigation's root cause is found; mission-redirect and parameter tampering are next.